Pneumatic L sealer

Use and maintenance manual

# 1、Foreword

1、Summarize

Thanks to buy our product, this machine are safe, practice , effect sealing packager.

2、Carefully for manual

- Please read carefully this manual before using machine.

- Please use machine after on top of machine knowledge.

- Please keep this manual, and read it at any moment.

- Please give the manual to end user.

- Due to ceaseless improve and perfect machine, our company reserve right to amend machine and manual.

- If have good suggestion for this machine or manual, please connect with  our company.

3、Safety notice

- Must use considerable breaker and power wire for this machine. If use big capacity breaker or small power wire, that make circuitry or parts damager.

- Please sure liquid would not leap out when packing liquid product. If not , damager would be made to the machine and the operator would possibly get an electric shock.

- Don’t use the machine in a very moist and humid environment, or a place full of a lot of vapor.

- Don’t use the machine in a place full of duct.

- Don’t put you hand on the parts for sealing.

- Don’t put any metal article on part for sealing avoid damage for sealing blade.

- The sealing time should be of 0.8-1.5s in general, the sealing blade would be damaged if the sealing time be set too long.

- The compressed air of 46kg/cm is needed when the machine works, the machine would not work well of the air pressure is too low；

- The frequency of sealing action when the machine is in the status of auto, otherwise there is the danger of inquire to product or the hand of the operator in the case of the failure of the sealing protective function（it is suggested that the interval  time to be set to 3-6 s）；

- The sealing blade, Teflon belt, neoprene rubber is easy to be worn after some time, so please prepare some damageable parts like these and examine and repair the machine periodically.

- The power of the machine should be turn off first when you want to replace the spare parts and please do it according to the right procedures.

4、features of machine

A.	This machine is widely used for the packaging application of these industries: food, toy, hardware, cosmetic, medicine, daily commodity, books, bamboo products, wooden products

B.	Suit for PVC、POF etc；

C.	The sealing blade is made of alloy, stick proof and high temperature –proof, with out carbonization and smoking when sealing.

D.	The sealing time is easy to be adjusted based on the thickness of the film,

E.	The product to be packaged is unloaded automatically by the conveying belt and the conveying time is adjustable；

F.	Sealing and shrinking for one time, safe and reliable, easy to operate, the part sealed of the film is firm and looks well；

G．the machine can working longtime continuum, which meet for large output

2、Machine dimension and crate dimension

GPL-12080 machine dimension

GPL-12080Cmachine dimension

GPL-12080 be packed dimension         GPL-12080 be packed dimension

3、Machine panel and each button name and function

1、Auto and manual switch

2、Main power

3、relayⅠ： seal bar up and down inverter time (in auto condition)

4、RelayⅡ：time before seal bar ready to seal

5、Relay Ⅲ：set sealing time

4、Machine parts illuminate drawing

1、machine total install drawing

| No. | name | Qua. |
| --- | --- | --- |
| 1 | Machine frame | 1 |
| 2 | Sealing system | 1 |
| 3 | Electrical connect system | 1 |
| 4 | Film frame system | 1 |
| 5 | Convey system | 1 |

# 2、machine frame parts drawing

| No. | Drawing No. | name | Qua. |
| --- | --- | --- | --- |
| 1 | 1-04 | undergird board | 1 |
| 2 | 1-03 | Jointing foot board | 2 |
| 3 | 1-02 | Lower frame | 2 |
| 4 | WGBZ001 | Foot | 4 |
| 5 | WGBZ002 | Foot wheel | 4 |
| 6 | WGBZ003 | boltM6X12 | 16 |
| 7 | WGBZ004 | nut M6 | 4 |
| 8 | 1-01 | Upper frame | 1 |
| 9 | 1-06 | Right sealing board | 1 |
| 10 | 1-07 | Middle tendon board | 1 |
| 11 | 1-05 | Left sealing board | 1 |
| 12 | 1-09 | Side tendon board | 1 |
| 13 | 1-01-02 | Support board of working table | 1 |
| 14 | 4-L | Runner of control box | 1 |
| 15 | 4-R | Runner of distributing board | 1 |
| 16 | 1-12 | Strengthen board | 1 |
| 17 | 1-01-01 | Strengthen board behind upper machine frame | 1 |
| 18 | 8 | distributing board | 1 |
| 19 | 02 | Cover of electric appliance | 1 |
| 20 | 1-08 | Hand wheel fix board | 1 |
| 21 | 1-10 | Steel tube 1 | 1 |
| 22 | 1-11 | Steel tube 1 | 1 |
| 23 | 3-23 | Switch seat | 2 |
| 24 | 01 | Working board | 1 |
| 25 | WGBZ005 | boltM6X10 | 8 |
| 26 | WGBZ006 | Hexangular screwM6X10+ washer 6 | 7 |
| 27 | 1-13 | Bearing base | 2 |
| 28 | WGBZ007 | Bearing 6205 | 2 |
| 29 | WGBZ008 | boltM8X20 | 5 |
| 30 | 3-17-1 | Slot of rubber 1 | 1 |
| 31 | 3-17-2 | Slot of rubber 2 | 1 |
| 32 | WGBZ009 | rubber 1 | 1 |
| 33 | WGBZ010 | rubber 2 | 1 |
| 34 | WGBZ011 | Teflon belt 1 | 1 |
| 35 | WGBZ012 | Teflon belt 2 | 1 |
| 36 | WGBZ013 | Urgent stop button | 1 |
| 37 | WGBZ014 | Start button | 1 |
| 38 | 3-25 | Air cylinder connect shaft | 1 |
| 39 | 3-24 | Air cylinder base | 1 |
| 40 | 3-27 | Air cylinder pin | 1 |
| 41 | WGBZ015 | Air cylinder | 1 |
| 42 | WGBZ016 | Electromagnetism value Connect bracket | 1 |

# 3、convey parts drawing

| No. | Drawing no. | name | Qua. |
| --- | --- | --- | --- |
| 1 | 2-1 | Rise & fall stand | 1 |
| 2 | 2-2 | stator | 1 |
| 3 | 2-9 | Right stator | 1 |
| 4 | 2-10 | Left stator | 1 |
| 5 | 2-10A | stator | 2 |
| 6 | 2．2 | Shaft of idler wheel 2 | 1 |
| 7 | 2．1 | Shaft of idler wheel 1 | 1 |
| 8 | 2-13-L | Left small stand | 1 |
| 9 | 2-13-R | Right small stand | 1 |
| 10 | 2-3 | Block cover | 1 |
| 11 | 2-6 | Motor install board | 1 |
| 12 | 2-17 | pressing plate | 1 |
| 13 | 2-15 | Extended roller | 2 |
| 14 | 2-16 | Extended roller pastern cover | 2 |
| 15 | WGBZ021 | Convey belt | 1 |
| 16 | 2-19 | Extended roller support bar | 4 |
| 17 | WGBZ022 | motor | 1 |
| 18 | WGBZ023 | chain | 1 |
| 19 | WGBZ024 | boltM4X16 | 4 |
| 20 | WGBZ025 | boltM4X10 | 8 |
| 21 | WGBZ026 | Washer 6 | 16 |
| 22 | WGBZ027 | Washer 6 | 12 |
| 23 | WGBZ028 | boltM6X12 | 12 |
| 24 | WGBZ029 | Hexangular bolt + spring Washer +WasherM6X25 | 2 |
| 25 | WGBZ030 | Hexangular bolt +WasherM4X12 | 4 |
| 26 | WGBZ031 | Hexangular bolt +WasherM6X12 | 4 |
| 27 | WGBZ032 | Chain wheel | 1 |
| 28 | WGBZ033 | Chain wheel | 2 |
| 29 | WGBZ034 | Connect block | 1 |
| 30 | WGBZ035 | boltM6X10 | 2 |
| 31 | WGBZ036 | Bearing 6001 | 4 |
| 32 | 2-8 | screw | 4 |
| 33 | WGBZ037 | Chain wheel | 4 |
| 34 | WGBZ038 | Bearing 51101 | 5 |
| 35 | WGBZ039 | nut M12 | 4 |
| 36 | WGBZ040 | Adjusted chain | 1 |
| 37 | 2-11 | Tightening wheel | 1 |
| 38 | 2-12 | Tightening wheel axle | 1 |
| 39 | 2-18 | Hand wheel axle | 1 |
| 40 | WGBZ041 | Hand wheel | 1 |
| 41 | WGBZ042 | washer | 2 |
| 42 | WGBZ043 | boltM8X55 | 1 |

# 4、sealing system drawing

| No. | Drawing no. | name | Qua. |
| --- | --- | --- | --- |
| 1 | 3-15 | Movable shaft | 1 |
| 2 | 3-1 | Upper Left stand on sealing box | 1 |
| 3 | 3-2 | Upper right stand on sealing box | 1 |
| 4 | 3-12-R | Upper sealing slot 2 | 1 |
| 5 | 3-12-F | Upper sealing slot 1 | 1 |
| 6 | 3-21 | Board of fixing corner | 1 |
| 7 | 3-20 | fixing corner | 1 |
| 8 | WGBZ046 | Spring 8X60X1 | 2 |
| 9 | 3-7 | Tension scabbard | 2 |
| 10 | 3-5 | Insulated cover 1 | 2 |
| 11 | 3-6A | Switch stand 2 | 2 |
| 12 | 3-5A | Insulated cover 2 | 2 |
| 13 | 3-8 | Switch stand 3 | 1 |
| 14 | WGBZ047 | Hexangular boltM6X16+washer 6 | 2 |
| 15 | 3．1 | Turn board | 1 |
| 16 | 3-11 | Cover of sealing slot 1 | 1 |
| 17 | 3-13 | Cover of sealing slot 2 | 1 |
| 18 | WGBZ048 | washer | 8 |
| 19 | WGBZ049 | Spring 8X45X1 | 4 |
| 20 | WGBZ050 | 一round hood bolt M5X14 |  |
| 21 | 3-18 | wire slot 1 | 1 |
| 22 | 3-19 | wire slot 2 | 1 |
| 23 | WGBZ051 | boltM6X30 |  |
| 24 | WGBZ052 | boltM8X12 |  |
| 25 | WGBZ053 | boltM5X20 |  |
| 26 | WGBZ054 | boltM4X40 |  |
| 27 | WGBZ055 | boltM5X5 |  |
| 28 | WGBZ056 | boltM4X6 |  |
| 29 | WGBZ057 | boltM6X40 |  |
| 30 | 3 | Front wire slot |  |
| 31 | 3 | Right wire slot | 1 |
| 32 | WGBZ058 | Sealing blade | 1 |
| 33 | WGBZ059 | boltM3X10 | 4 |
| 34 | WGBZ060 | boltM3X12 | 1 |

5、send film system

| No. | Drawing no. | name | Qua. |
| --- | --- | --- | --- |
| 1 | 4-01 | Fixing board | 1 |
| 2 | WGBZ061 | BoltM8X16 | 13 |
| 3 | WGBZ062 | washer | 13 |
| 4 | WGBZ063 | Pastern cover | 2 |
| 5 | 4-07 | Support shaft | 2 |
| 6 | WGBZ064 | Club handleM8 inside tooth | 2 |
| 7 | 4-10 | idler wheel | 2 |
| 8 | 4-03 | Side board 2 | 1 |
| 9 | 4-06 | Support shaft | 2 |
| 10 | 4-8 | Pressing plate | 2 |
| 11 | 4-10 | idler wheel | 2 |
| 12 | 4-9 | Movable orientation plate | 2 |
| 13 | WGBZ065 | Club handleM8X30out side tooth | 3 |
| 14 | 4-02 | Side board 1 | 1 |
| 15 | 4-04 | Adjusted board | 1 |

6、distribution panel parts diagram

| No. | code name | Name |
| --- | --- | --- |
| 1 | K1 | 220V middle relay |
| 2 | K2 | 220V middle relay |
| 3 | K3 | 220V middle relay |
| 4 | K4 | 24Vmiddle relay |
| 5 | KM1 | Sealing blade contactor |
| 6 | QF1 | Sealing blade loop breaker |
| 7 | QF2 | Control loop breaker |
| 8 | T1 | Sealing blade transformer |
| 9 | T2 | Magnetic transformer |
| 10 | C1 | capacitance of the transporting motor |

5、machine technology parameter

| model | GPL-12080 |
| --- | --- |
| Power supply | 1 phase 220V 50Hz 1 phase 110V 60Hz |
| power | 1.2kw |
| Max sealing size | L120*W800 |
| Machine size | L2920*W1350*H1270 |
| weight | 500kg |

6、machine installation

- Remove four side boards after open upper cover of the crate；；

- Carry out the main machine, place the machine on the place ground steadily；

- Unpack the protective film wrapping on the machine.；

- Put up one side of the machine bottom, install two foot wheel of this side; then put up other side again, install other two foot wheel；

- Fasten the four foot bolts at the bottom, the machine can move only by the wheel；

- Take out of the reel holder, then fix to side of the machine with the bolt；

- Use the bolt from machine parts fix the reel holder on side of the machine

according to volt from nameplate, and     connect with wire，

remark：with fail connect earth。

7、machine operation method

# install film drawing

- Connect air compressor，adjusted to 4-6kg/cm2,that sealing blade upper frame will auto rise；

- Turn the power on, set the emergency button on and the operation mode to be manual

- Set the sealing time according to the thickness and characteristics of the shrink film 0.5-1.5s in genera（the appropriate sealing time leads to the film to be cut off completely and s good sealing effect. If the sealing time is too short, the film can not be cut off, or the sealing blade, blade slot and the Teflon belt would be easily damaged if the sealing time to be set too long）；

- Usually, set the sealing time a litter longer when turn the power on at the beginning due to there is no any accumulation of the heat on the blade. Set the sealing time a little shorter than beginning due to the accumulation of the heat on the blade；

- Set the transporting time according to the size of the product to be packed and the specific requirements for packing；

- Place the film reel there between the two poles on the reel holder，（make the open side of the film toward to the operator），position the two poles and fasten them；

- Thread the film through the perforator, separate the two layers, get it surround the working table；

- According to size of goods, adjusting adjusted handle, which on bottom of machine，sure center wire of products equal of sealing blade

- use film turn left and pull to sealing area turn left, put the products between of shrink film and working table, than turn left and pull the film and products to sealing area.

- Keep a distance of 1/2 height of the product between the product and sealing blade in order to have enough film for shrinking；

- Button the green button, machine will sealing.

- After sealing, the upper frame auto rise, convey belt is working by machine, and to put the goods to shrink tunnel.

- Turn on auto position switch, machine will auto sealing. Set interval time(time for front sealing and finish convey with times for next sealing. time set about 3-6s)；

- Press sealing star button, here, machine according to set interval time in advance to sealing continually.

8、machine maintenance

A.、Clean the working table and the transporting belt after the use every day；

B、Clean the sealing blade periodically .Notice: clean the sealing blade by a piece of dry cotton with the release agent, Don ’t use any metal article scratch the sealing blade.

C、The movable parts(such as transmitting chains, bearing base) needs to be oiled with lubricant often；

D、The sealing blade, Teflon belt, rubber must be kept well. If the sealing blade or the Teflon is worn or damaged, replace it with a new one soon

E、Turn the power off before repairing let professional to do it；

F、The procedures of replacing the sealing blade：

1、turn the machine power off；

2、make the curl part of the two ands of the sealing blade straight（notice: please do it lightly in order to avoid the rupture of the nylon cover of the blade clamp ）；

3、unfasten the  screws on the tow ands of the blade clamp, take the worn sealing blade out；

4、put one and of the new sealing blade into the slot of the blade clamp, 5mm left outside of the clamp, then tighten the screws and curl the extended blade outside the clamp；

5、put the new sealing blade into the ceramic blade slot lightly, then put the other and of the sealing blade into the slot of the other blade clamp；

6、straighten the sealing blade , fasten the screws and curl the two ends of the sealing blades；

9、machine circuit diagram

10、troubleshooting

| trouble | cause | solution |
| --- | --- | --- |
| Sealing blade not heating | Breaker off | Check reason and put it on |
|  | Sealing blade damaged | Replace new one |
|  | Transformer damaged | Test the output of the transformer when sealing, If no 54v output, please replace new one |
|  | The device protect the sealing blade from worn was not set well | Keep distance 3-5mm for the screws and avoid sealing blade worn bolt |
| Sealing blade can be heated, but can not cut off film | Partial damage for the sealing blade | Replace new one |
|  | Something unknown on the sealing blade | Clean the sealing blade by a piece of dry cotton and the release agent |
|  | Damaged for Teflon belt | Replace new one |
|  | Damaged for rubber | Replace new one |
|  | The bolt of the fixing sealing slot be unfasten, leading to sealing slot uneven | Level the sealing slot and fasten screws |
| Convey system do not work | Transport time is set to be 0 | Adjust transport time |
|  | Breaker off | Put it on |
|  | Transport device can not move | Check chain of the transport system |
| Shake of the convey belt | The transport belt is too tight | Adjust it again |
| Press start button, but machine not work | Emergency switch is on | Turn the emergency switch off |
|  | Breaker off | Check circuit, put it on |
|  | avoid sealing jiggle switch not adjust well | The three jiggle switch should be in free status when sealing bar goes up |
|  | Electromagnetic valve damaged | Clean core of the electromagnetic, replace new on if necessary |
| Sealing upper frame fall to right place but can not sealing | Jiggle witch not set well | Make jiggle switch working, if damaged ,please replace new one |