Use and Maintenance Manual

GPL-5545T+GPS-4525

ONE. Foreword

1、Summary

Thanks a lot for choosing our products ,this machine is a safe ,practical and high efficient constant temperature shrink packager.

2、Attention of this manual

- Please read this manual carefully before use the machine；

- Please operate the machine after have its knowledge expertly and related attention；

- Please keep this manual well as reference at any moment.；

- Hand this manual to direct user without fail；

- We keep the rights to modify this manual because of the machine function is improving and advancing continuously；

- Please contact us if having any good suggestion in this manual or our machines；

3、Safety attention

- Use equivalent breaker and wire apply to the machine’s capacity ;circuit and units is easy damaged if adopts lower capacity breaker or thinner electrical wire；

- To ensure unable leak out when the machine pack liquid product ,it may cause damage on machine or get electric shock when pack imperfectly sealed liquid；

- Do not let the machine to touch plentiful vapour or it is not allow to use this machine in heavy humidity environment；

- Do not use or put the machine on dust occasion；

- Don’t put any metal article on part for sealing avoid damage for sealing blade.

- The sealing time should be of 0.8-1.5s in general, the sealing blade would be damaged if the sealing time be set too long.

- Please do not touch the place where stick with hot caution sign ,it is dangerous in hot when the machine on running；

- There are some wearing part like blade/temperature proof tape/temperature proof rubber and it will be consumed during its operation, so please keep some replacement and inspect the machine timely.

- Cut off power when replace spare part and follow the correct process.

4、Machine Function

- It is suit to do surface packaging for food stuff、electronics、toy、bamboo and wooden appliance、hardware、cosmetic、medicine、book、electric appliance and so on; The package is characteristic with beautiful appearance 、moistureproof   and not easy broken ,so it improve product’s impress but in lower cost.

- Hang together advanced shrink blowing technology and made by improved but unique design, the blowing is even and shrink effect is perfect；

- Adopts stainless steel heating tube with long life time and high efficiency；

- The conveyer adopts new type roller that covered by silicon ,high temperature proof、wearable、non burn film and not change for long time use；

- Choose well-known electric units like switch and temperature controller etc.，stable works and lower fault；

- Convey motor and blow motor are adopted from famous brand ,strong power and can bear long working time continuously；

- Heat up the oven after blower working ,the machine is furnished with pre-stop device which can prolong its life；

- The machine is applicable to PVC、PP、POF etc shrink film.

TWO、Crate size and surface dimension

1、Surface dimension

2、Crate size

THREE、Control panel and name of each units

1．Power switch：  switch off / on main power supply；

2．Startup indicator：indicate control power switched on or not；

3．Heat indicator：indicate heating system work on or not；

4．Blow indicator：indicate blowing system work on or not；

5．Temperature controller：  set up heating temperature；

6．Electrical speed controller：adjust the feed speed of conveyor belt；

7．Emergent stop：  Cut off control power；

8．Startup switch：  turn on control power；

9．Heating switch：  Control heating system work on or not；

10．Blowing switch：  Control blowing system work on or not；

FOUR. Parts illuminate drawing

1、Drawing of main structure

| No. | Name | QTY | No. | Name | QTY |
| --- | --- | --- | --- | --- | --- |
| 1 | Foot support | 1 | 6 | Control system | 1 |
| 2 | Lifting system | 1 | 7 | Sealing structure | 1 |
| 3 | Blowing system | 1 | 8 | Feeding structure | 1 |
| 4 | Feeding system | 1 | 9 | Transporting structure | 1 |
| 5 | Heating system | 1 | 10 | Electrical structure | 1 |

2、Instruction of parts on switchboard

| No. | Code | Name | Qty |
| --- | --- | --- | --- |
| 1 | QF | Loop control breaker C32N1PC2A | 1 |
| 2 | KM1 | Blowing system contactor LCD-D0910 | 1 |
| 3 | KM2 | Heating system contactor LCD-D4011 | 1 |
| 4 | KM3 | Loop control contactor LCD-D0910 | 1 |
| 5 | KT1 | Pre-stop time relay AH5B | 1 |

3、Blowing system chart

| No | Name | QTY | No | Name | QTY |
| --- | --- | --- | --- | --- | --- |
| 1 | Oven inner shell welding part | 1 | 12 | GB＿CROSS＿SCREWS＿TYPE1 M5X25-25 | 20 |
| 2 | Oven out shell | 1 | 13 | GB＿CROSS＿SCREWS＿TYPE1 M5X45-45 | 4 |
| 3 | Circumfluence fan cover | 1 | 14 | Inner hexangular knob M6X16 | 4 |
| 4 | Fan cover | 1 | 15 | GB＿CROSS＿SCREWS＿TYPE1 M5X35-35 | 4 |
| 5 | down closing board welding part | 2 | 16 | Inner hexangular knob M8X16 | 4 |
| 6 | Fan | 1 | 17 | heat insulating curtain | 2 |
| 7 | Heat insulating board gasket | 20 | 18 | Clip slot of heat insulating curtain | 2 |
| 8 | Heat insulating board at left and right | 2 | 19 | GB＿CROSS＿SCREWS＿TYPE1 M4X10-10 | 4 |
| 9 | Heat insulating board gasket 44-48 | 4 | 20 | Thermocouple support rack | 1 |
| 10 | Heat insulating board at front | 1 | 21 | GB＿CROSS＿SCREWS＿TYPE1 M4X8-8 | 1 |
| 11 | Heat insulating board at behind | 1 |  |  |  |

4、Heating system chart

| No | Name | QTY |
| --- | --- | --- |
| 1 | Heating thread support rack | 1 |
| 2 | Heating thread junction box | 1 |
| 3 | Cover of Heating thread junction box | 1 |
| 4 | Heating thread | 3 |

5、Conveying system chart

| No | Name | QTY | No | Name | QTY |
| --- | --- | --- | --- | --- | --- |
| 1 | Convey drive axes | 1 | 11 | Driven chain wheel fixing part | 2 |
| 2 | 08B-21 Chain wheel fitting part | 2 | 12 | JIS B 2804 HOLE USE 52 | 2 |
| 3 | 08B Chain | 2 | 13 | Locate stop ring fixing part | 2 |
| 4 | Convey driven axes | 1 | 14 | Ball bearing 6205 GB T276 | 2 |
| 5 | Convey roller | 76 | 15 | JIS B 2804 SHAFT USE 52 | 2 |
| 6 | Heat-resistant silicon tube | 76 | 16 | Inner hexangular screw M10X80 | 2 |
| 7 | 06B Chain | 1 | 17 | Inner hexangular screw M10X20 | 2 |
| 8 | 06B-24 Chain wheel fitting part | 1 | 18 | GB＿CONNECTING＿PIECE ＿KEYS＿CSK C6X40 | 1 |
| 9 | 06B-21 Chain wheel fitting part | 1 | 19 | GB＿CONNECTING＿PIECE ＿KEYS＿CSK C6X70 | 1 |
| 10 | JWD motor 180W | 1 | 20 | GB＿CONNECTING＿PIECE ＿KEYS＿CSK C4X25 | 1 |

FIVE、Technical parameter diagram

| Model | GPL-5545T+GPS-4525 |
| --- | --- |
| Power supply | 1Ф 220V 50/60 |
| Power | 8KW |
| Oven entrance size | W450*H250 |
| Machine’s dimension | L1000*W750*H1480 |
| Work efficiency | 2000-3000/h |
| Weight | 160kg |

SIX、Installation

- Open up top cover of wooden case and take away four side boards；

- Carry out main machine’s body and put it on ground smoothly；

- Adjust foot screw at bottom to make machine on flat ,and prevent glide when machine is running；

- To facilitate for transportation before delivery ,the feet has been take out and put in carton;therefore customer needs to open this carton and assembly it by screw；

E. Please connect electrical wire according to displayed voltage on name plate,notice: must be ground.

SEVEN、Operate methods

- Turn on main power switch and press startup button,then turn on blower switch；

- It must turn on blower first and then heat up.（SM-5030 has two blowing motors）

- Switch on electrical speed controller at panel,convey roller and related chain will move along with the operation; Convey speed can be adjusted by the knob at speed controller；

- Turn on heating switch at panel,and turn the knob at temperature controller to set parameter from 150-170℃；

- After the temperature reached at preset date,the heat indicator is off as well as heating tube will stop to heat up；

- Please turn off heating switch before end of operation,the blowing will shut off automatically till continuous run within pre-stop time；

- Turn off blowing switch after blower stop and then cut off main power supply switch.

EIGHT、Maintenance

  - Clean away the leftover and dust on convey roller after finishing work；

  - Check lubricant in the gearbox of convey motor termly；

  - To do a general inspection for machine’s whole performance month open the switch box to clear dust or sundries；

  - Refill lubricant timely for chain and other run parts.

NINE、Circuit diagram

TEN、Trouble shooting

| Failure status | Reason | Solution |
| --- | --- | --- |
| Bad shrink effect | Temperature is too lower or higher | Adjust temperature |
|  | Conveyor belt is run too fast | Adjust convey speed |
|  | Convey roller is not working | Add lubricant |
| Noise is too big | Lack lubricant | Refill lubricant |
| Heater is not controlled | Temperature controller is broken | Replace temperature controller |
| No or lower temperature after heat up | Input voltage is abnormal | Check input voltage |
|  | Power connect wire loose | Check power connect wire |
|  | Heating tube is burned out | Replace heating tube |
|  | Heating switch is broken | Replace heating switch |
| Pop stop | Breaker is jump up | Check circuit and then turn |

ELEVEN、Packing list

| No | Name | Specification | QTY |
| --- | --- | --- | --- |
| 1 | Main machine |  | 1set |
| 2 | ‘十’Screw driver |  | 1 pc |
| 3 | Manual |  | 1 pc |
| 4 | Breaker | C32N1PC2A | 1 pc |