Index

1, the safety precautions ...................................................................................2

2, the safety operation precautions....................................................................3

3. the mechanical specifications .......................................................................5

4, the mechanical installation ...........................................................................8

5, mechanical debugging and operation ..........................................................10

6, mechanical adjustment.................................................................................24

7, mechanical maintenance...............................................................................30

8, troubleshooting.............................................................................................34

9, circuit diagram..............................................................................................38

10,electrical component list..............................................................................40

First .the safety precautions:

1,Please read all the related instruction before operating the machine.

2, In order to avoid accidents, please keep the workplace well ventilated, and pay attention to the damage of packaging which may cause liquid or gas leakage.

3, maintenance person must read the machine maintenance instructions carefully, before the maintenance work.

4, confirm the power has been cut off, before the maintenance work.

5, during machine running, if any accident occurs, turn off the power at first place, and then make the appropriate measures.

6, the machine is not suitable for packaging explosives products. In addition, if you want to package small items or liquid, powder, should first have them packed in boxes,tanks, bags and other packaging,

7, the machine does not apply to the PVC film, because the PVC material is easy to damage the machine's knife , if you must use PVC film, the knife must be a special material. If PVC is used for POF knife, the warranty is automatically invalid.

8, If modify the machine without authorization, the occurrence of any accident will not be responsible by manufacturer.

9, all air pressure pipes and cylinders can not have oil or water and other contaminated items, if these pollutants found, the warranty become invalid.

10, if you have any questions, please contact us free.

11, Before delivery, all the Five-start handle (Generally used for feeding box pin wheels fastening , membrane position-fixing rod fastening, the front transport  material keep-off Rod fastening handle ) will be wrapped with white sealing tape to prevent from loosening during the transportation,which may lead to the lost of the handles. After the installation of the machine, the customer can be removed or retained the sealing tape according to the actual situation.

Second. the safety operation precautions:

1, None except the operator can operate the machine. When the machine is in automatic operation, the operator can not place the hand under the sealing knife or within the range of the electric eye, so as to avoid the accident.

2, When the machine is running, the operator can not stretch out hands to the front and the rear of conveyor rolling part, in case the hand was jammed or caught into the machine.

3, When the machine automatically run, should keep the safety door close, to avoid any contact with the sealing device and cause injury by burns,and other hazards.

4, When the machine press to the product and alarm, or other failure occurs, should first press the emergency stop switch, the operation mode should change from automatic operation to manual operation. After all the failure being cleared, release the emergency stop switch, turn back to automatic operation.

5, pay attention to the film sending rubber roller and the needle roller part, when the machine running,must keep the safety door close, do not touch by hand, in case any damaged caused.

6, if the electronic tape cracked, must be replaced by new one, so as not to affect the quality of sealing and sealing knife life. When there is film on the knife or other debris, need to use cotton towel clean the knife. When cleaning, the emergency stop switch must be pressed and the machine is in manual operation mode. When doing this cleaning, turn off the main power supply to ensure safety.

7, before connecting to the power source and running the machine, you must first take off the moisture beads in the machine

Third.the mechanical specifications;

1、Machine Specification

| Machine Model： | ZF-6352 |
| --- | --- |
| Machine Size L×W×H（mm）： | 1950×1570×1310 |
| Sealing Knife Size mm: | L：630 W：515 |
| Packing Products Size L×W×H（mm）： | （60~560）×（60~430）×（10~180） |
| Max.Packing Width″： | 25″ |
| Production Capacity: | 40Pcs/min |
| Conveyor speed m/min: | 26M/min |
| Packing Material： | POF、PE |
| Sealing Knife Temperature℃： | 180-230℃ |
| Voltage V： | 220V/1P |
| Motor Power W： | 320W |
| Heating Power KW： | 2.5KW |
| Total PowerKW： | 3KW |
| Ross Weight Kg： | 870Kg |
| Gas consumption KG： | 6kg/sp.cm |

2、Machine Size

Unit：mm

3、Operation Panel

Forth.Machine Installation;

1, Installation location:

- The machine should be installed in a bright, dry place.

- The machine should be installed away from environment of dust, explosive and inflammable,corrosive.

(3) Do not place the machine too close to the ventilation system, which would case sending of unstable.

2, installation:

(1) After the installation site is selected, move the machine to the intended location to match the production line.

(2) mechanical height adjustment: use the wrench to loosen the lock nut under the rack, and then adjust the height adjustment nut, until the required mechanical height is reached, and finally tighten the lock nut. (Figure 4.1)

(3) level of mechanical adjustments: use the wrench to loosen the lock nut under the rack, take the sealing machine conveyor as base to adjust the height of the machine, lock nuts after the machine conveyor belts in the horizontal plane.

(4) Power Connection:

A. Turn the machine power switch to OFF.

B. The main power switch to OFF, confirm the voltage is correct, then have the sealing machine power connected.

C. Check all the machine part in normal condition, turn the machine power switch to ON, then the machine into the operating state.

(5) Pneumatic device: As shown in Figure 4.2, the air pressure throat connected to the machine's air pipe, open the intake valve, and then rotate the air adjustment device, so that the air pressure maintained at 6kg / cm2 or more.

Fifth.mechanical debugging and operation;

1、Machine Installation

（1）Sealing Machine Control Function Explanation

| Diagrams | Application Function |  | Diagram | Application Function |
| --- | --- | --- | --- | --- |
|  | Off Safety door ON Safety door |  |  | Power supply indicator |
|  | Set the temperature of heating tube for the side sealing knife,to control the sealing performance. |  |  | When select 1 or ON，the sealing knife hearing tubes start working, will heating to the set temperature. |
|  | Set the temperature of heating tube for the front sealing knife,to control the sealing performance. |  |  | Click it down, the machine will stop working immediately. To start the machine again, should loose the button. |

Diagram 5.1

2, touch screen operation and its function explanation

(1) to open the main power switch, touch screen display the home page as shown

【home page】

Click anywhere on the screen to automatically enter the automatic page

【Automatic page】

A. End Sealing: Click, sealing ended.

B. Start: Click the "Start" button, the device into the running state.

C. Reset: When the device is in alarm, click the "Reset" button to cancel the alarm and enter the normal preparation state.

D. Stop: Click the "Stop" button and the device stops.

Select "manual screen" automatically enter the manual page:

【Manual page】

A. Manual Seal: Click, manually sealed once.

B. pulling film: click, feed film and pull film start; release, action to stop.

C. Front conveyor belt,click, the front conveyor enter the manual operation.

D. after the delivery: click, the rear conveyor enter the manual operation.

E. blade up, click,the blade lift up..

F. blade down: click,the blade down.

Select "parameter screen" ,automatically enter the parameters page:

【Parameter page】

A. Sealing time delay: Set the time of feeding film

B. Sealing time: Seal cutting time.

C. Film feeding time before: every action of sealing, the time to feed the film.

D.Delayed feeding time: the time of delayed pulling film when products-detecting eyes detected the product.

Select "function page" automatically enter the function page:

【Function page】

A. program switching: click "transparent" product and "solid"product to choose the two program.

B. machine close/open: choose “open” the device automatically start.

C. Horizontal / Vertical: Click, "Horizontal Detection" and "Vertical Detection" mode switching.

D. Connecting conveyor belt: "open" and "close" switch.

E. Heating switch: click, "heating close" and "heating on" two mode switch.

2. Function debugging

(1) When the machine into running state,switch to the automatic mode, check whether the conveyor is running normally, whether the conveyor surface is in the middle of the wheel, if there is deviation, please refer to the next chapter conveyor belt adjustment, after adjustment,switch the machine to manual mode.

(2) The width of the package mentioned in this manual is expressed as "W" and the height is expressed by "H" and the length is expressed by "L" (Figure 5.1)

(3) shrink film width calculation method: shrink film width = (W + H) + (76~127)mm.

(4) tripod and conveyor belt adjustment

A. Tripod height adjustment: Figure 5.2, turn the hand wheel to adjust the height of the tripod, about (H + (5~10)mm packaging).

B. Conveyor width adjustment: release the adjustment handle, so that the conveyor belt into a stepless adjustable state, adjust the guide rod to adjust the conveyor belt width, about (W + 1/3 H)

C.Conveyor belt horizontal position adjustment: Hold the adjustment handle C, and hold the adjustment rod D, the front conveyor belt part can move along the guide rod, adjust to the appropriate position and then release the adjustment rod.The adjustment is complete. (The distance from the guide rod to the product is 1 / 3-1 / 2 of the Product height.)

D. ( Figure 5.3): press the “sealing blade lift “button (        ), seal blade rise, press the “sealing blade fall ”button (          ), sealing blade down, the appropriate height of the sealing knife generally adjusted according to product height ,the most appropriate (½ H).

(5) Load shrink film to the film fixing roller.

A. As shown in Figure 5.4, the shrink film is placed on the film feed roller. Note: that the opening side of the shrink film must face the side of the positioning of rod B.

B.If the height of the packing product H ≦ 20mm, the left side of the film should be placed in the 0 scale line. If the height of the package H> 20mm, the film position is based on the vertical and horizontal tripod vertical height. (If the display value is L1, move the left end of the film to a size of 1 / 2L1.)

C. After adjusting the film position, move the positioning rod on both sides, adjust it to both ends of the film, and then tighten the lock handle to fix.

(6) shrink film feeding parallel adjustment. (As shown in Figure 5. 5)

A. Loosen the fastening handle and turn the handwheel to adjust the scroll wheel position.

B. According to the upper and lower triangular plate height value H1, the scroll wheel is fixed at the scale position of ½ H1.

（7）Method for loading the film（Figure 5.6）

- As shown in the figure of Figure 5.7.

A.lift handle(5.7A),so the rubber roller(5.7B) up, at the same time, turn the pin rollers up.

B.through the film as in the diagram of 5.6, then reset the handle and pin roller to former position.

C.Depending on the packaging products, the number of needle(pin) roller is different. Loosen the fixing handle (5.7D) to slide the pin roller device and increase or decrease the number of needle roller as needed.

(9) Sealing blade heating

Turn on the heating switch to 1 (select       ), and set the front and side seals blade to the appropriate temperature . (See Table 5.1 for temperature adjustment)

| Film | Needed Temperature | Film | Needed Temperature |
| --- | --- | --- | --- |
| PE Film | 240℃~260℃ | POF | 200℃~220℃ |

(10) When the temperature reaches the default degree, press the pull film switch (    ) once, then the pull device will pull the shrink film, if the film is not pulled, please check the film is placed correctly or not.

(11) If the above action is normal, press the manual sealing switch (          ) once, at that time the sealing blade will carry out the sealing action, and complete the sealing and cutting of the shrink film.

- Repeat the operation several times as described in (10, 11), until the shrink film scrap can coiled on the scrap-winding roller for 2-3 turns, then the sealing machine can be operated automatically.

(13) Switch the machine to automatic mode and place the product to be packed on the conveyor.

Note: Both hands should be completely away from the conveyor surface to avoid danger.

(14) adjust the seal to the best condition

A. Adjust the pre-sending (feeding) film: pre-feeding film length is best 1 / 3H, then the best shrink effect. (Figure 5.9 size A)

Adjustment method:

a. When the product height H <100mm, the reserved pre-feeding film length is too long, could adjust the photoelectric and sealing blade distance L1 shorter.

b. Product height H ≥ 100mm, set L1 to the maximum still not enough, can adjust reserved pre-feeding film / product front reserved time, to change the length of the film, the longer the time, the longer the film will be.

B. Adjustment (extend seal / product rear remaining time) method: to extend the seal time, according to the different electric eye induction mode. However, regardless of which mode adopted,adjust(Figure 5.9) size B to the length of 1 / 2H can get the best shrink performance.( The definition of extend the seal length is related to the way and principle of the electric eye.)

C. Different shrink film requires a different sealing time, generally about 0.3-0.6 seconds, depending on the sealing situation. Sealing lines should be cut off and no holes, if the cutting off is nonuniform, may caused by temperature overheating, could adjust the sealing time or sealing temperature.

(15) If the sealing line is satisfied, the sealing machine debugging is completed.

3, The machine function features

(1) The machine has a safety protection function and alarm device.

(2) sealing system can carry out the sealing action continuously.

(3) simple operation and can be used with different sizes of packaging products.

(4) The machine adopts PLC and electric eye control.

(5) electric eye devices including the horizontal eye(Fig.5.11) (PH1, PH3) and vertical electric eye(Fig.5.11) (PH2) two kinds. General products packaging use the horizontal electric eye, thin products packaging use vertical electric eye. In addition, the horizontal mode has wait-material function, which is controlled by the feed photoelectric (PH1). The vertical mode controlled by R1 intermediate relay, each time the sealing action finished once, the front conveyor stop one time.,suitable for connecting to conveyor in the front side, and products placed closely. Without R1, the conveyor won’t stop. In this case, suitable for connect to hand-push conveyor.

(6) According to the physical characteristics of packaging items, select the electric eye sensor mode, there are two kinds of modes, the standard mode and view compensation mode (Figure 5.11).

A. When the packing products is solid and of regular shape, adopt standard mode (Figure 5.11 (a)). In this mode, the electric eye captures the last point of the package, and then sends the instruction to the PLC, which controls the delay relay to start the timing. (Principle: such pack product will shield the electric eye radio, when the last point through, the electric eye restore the shot. Using this transaction of electrical signal to control the relay.

B. When the packaging items are transparent or of irregular shape (especially the objects have holes, can light through), should adopt the view compensation mode (Figure 5.11 (b)). In addition, when few products are packaged together side by side, and there is a gap between the products that could allow the light to pass through, at that time the view compensation mode should be adopted too. In this mode, the electric eye captures the first point of the product, and then sends the instruction to the PLC, and controls the delay relay to start timing. (Because before such product complete through the electric area,the electric eyes already restore shot, for there are gap between the products ,or for the irregular shape. At this condition, the standard mode is not effective. And should adopt view compensation mode,which has longer delay sealing time.)

(7) The machine can be used for the POF and PE shrink film, if you want to use PE film, please use the PE special knife, and affixed with heat-resistant tape, so that the upper sealing knife will not be in direct contact with PE film.

4, normal operation

(1) Start procedures

A. Turn on the power. (    )

B. Turn on the heater and let the temperature rise to the default. (    )

C. Switch the operating mode to automatic.

D.Put the pack product into the conveyor, sealing action finish automatically.

A The machine is equipped with two emergency stop device, if any abnormal conditions found, press this key, the sealing machine turn into the shutdown state, at that time,the power indicator light from the stability to flash.After the  abnormal situation settled, release this Key, the machine will be able to run normally., the power indicator light return steady light. (       )

(2) shutdown procedures:

A. First turn off the heater, so that the electric tube cooling, but this time there is still more than the heating tube temperature, pay attention to avoid burns. (      )

B. Then turn off the main power OFF. (      )

C. To close the air pressure, pay attention to its sealing and cutting part will be due to loss of wind pressure and down, this time should not be close to the machine, so as to avoid danger. But need to first open the air pressure source switch.

(2) shutdown procedures:

A. First turn off the heater, so that the electric tube cooling, but this time heating tube still with high temperature, pay attention to avoid burns. (select      )

B.Stop the machine, in case when start the machine nest time, the machine will work automatically.

C. Then turn off the main power OFF. (select      )

D. To close the air pressure, pay attention to its sealing and cutting part will go down due to loss of air pressure, this time should not be close to the machine, to avoid any danger. But when start the machine should open the air source switch in advance.

Sixth. mechanical adjustment;

1.Attention:

Before ex-mill, the machine has been carefully adjusted, if not necessary, please do not arbitrarily modify it, but the professional operators can make adjustment according to different packing products.

2.Machine adjustment

(1) shrink film feed section (Figure 6.1)

A. Delivery status

a. When the swing arm is in the position of Figure A, the swing arm is sensitive to the proximity switch, and the proximity switch controls the feed motor to stop.

b. When the swing arm is in the position of Figure B, the swing arm is far from the proximity switch, the proximity switch is not sensed, and the feed motor is running. (Note: when the pulling-film part is working, pull the arm to the position shown in Figure B.)

B. Induction adjustment

a. Loosen the screw on the swing arm, move the swing arm along the axis of rotation, adjust the distance between its flat end and the proximity switch (usually 1mm), so that the swing arm and proximity switch induction is good.

b. In addition, the proximity switch can be moved along the groove in the fixed seat, in the adjustment of the pull film tension increases, and vice versa is reduced.

(2), shrink film feeding parallel adjustment. (Figure 6.3)

A, the rear conveyor belt parallelism adjustment: (Figure 6.3A)

a.When the belt is too loose, loosen the screw 1, then turn the screw 2 counter-clockwise, push the rolling axle forward, and gently press the belt till it tight.

b.When the belt is too tight, turn the screws 2 on both sides of the machine clockwise to adjust the rolling axle till the belt get the desired tightness.

c.When the conveyor be partial to any one side of the screws, turn screw 2 counter-clockwisely, to increase the pressure between rolling axle and the belt. Or turn screw 2 at the other side of the machine clockwisely, to decrease the pressure between rolling axle and belt.

B. The front conveyor belt part: can refer to the adjustment of the rear conveyor belt. But the adjustment direction is opposite to the direction for adjusting the rear conveyor.

Note: After adjusting the screws, let the machine run for about ten minutes. If the conveyor belt is not offset, the adjustment is completed.

- , Tightness adjustment of the sealing device

A.put a piece of white paper between the sealing knife and sealing seat, select the manual mode for sealing, and then check the sealing knife pressure on the white paper is of average strength or not. If discovery there is any non-average, to relax the blade fix screw 1, rotate screw 2 counter-clockwisely, adjust to the average strength, then lock the fixed nut 1.(Figure 6.4)

B. When the fine adjustment finished, but the sealing device still not even, or there is obviously didn’t cut off and non-strong phenomenon, you need to re-adjust the sealing knife, the steps are as follows:

a. First turn off the power, and then unplug the air pipe, and start adjustment till the temperature go down.

b. Remove the fastening screws on the shield and remove the shield.

c. If the sealing knife is damaged, you need to replace the sealing knife, and then adjust according to step A.

(4), sealing protection device part:

A.This is the protection device designed in the sealing area of the machine, which can effectively prevent the sealing knife from accidentally cut on the packing products and protect the sealing knife and the packing product. If there is no such device, when the sealing knife down for sealing action, and this time the packing product just staying at the sealing area, the sealing knife cut on the packing product, resulting in sealing knife and packing products damage.

B.When the machine is made, the sealing protection height is set to 5mm, that is, the height of the package product is 5mm or more (including 5mm), the device will be protected, 5mm below does not. If need to pack products whose height is less than 5mm and make the device protected,should adjust the magnetic switch on the cylinder, move the switch to the cylinder bottom direction. the specific adjustment method see the following principle.

C. working principle:

a. As shown in Figure 6.5, the cylinder is driven by the chain and gear to promote the sealing device to carry out the sealing action . There is a magnetic switch PS1 as shown in Fig6.5 on the cylinder. When the piston of the cylinder reaches the stroke position where the PS1 is located, a safety sealing signal is generated. Allow the piston to continue to run to the cylinder bottom point to complete the sealing action. The sealing time is over and the piston returns.

Fig.6.5                                Fig.6.6

b. As shown in Figure 6.6, the proximity switch is fixed to the knife (blade)holder. The trigger roller is fixed between the knife holder and the shield and can move up and down along the positioning hole of the upper knife holder. When the guard plate is subjected to the upward force, the trigger roller triggered and moves to a certain height and is detected by the proximity switch, then the proximity switch will issue an abnormal sealing signal, control the cylinder immediately return to prevent the seal knife accidentally cut the packing product.

C. Under normal circumstances, the safety seal priority to the abnormal sealing signal, abnormal sealing signal does not work. But when sealing if there is packing product in the sealing area, the shield pressure to the packing product and the trigger roller has triggered an abnormal sealing signal in the product’s height (trigger principle refer to the above point b), and priority to the set security sealing signal. So before the sealing signal send, the cylinder has led the sealing device bounce, and issued an alarm to prevent the sealing knife cut on the packing product and cause damage.

D. Magnetic switch on the cylinder position adjustment: adjust each time to 1mm unit, when the magnetic switch position is more backward, then the security seal signal triggered later, on the contrary,the earlier. Note: For non-professionals, please do not adjust privately.

E. Trigger roller and proximity switch to adjust the distance: Loosen the screws on the trigger wheel, adjust the height of the trigger wheel up and down, the shorter the sensing distance, the faster the trigger time, and versa vice. Note: For non-professionals, please do not adjust yourself.

F. In addition, if there is obstruction between the trigger roller and the proximity switch , the device will lose the role of protection.

5.the scrap winding part(As Fig.6.7)

(1) Loose and remove the nut firstly, and then remove the fixed disk. After removing all the scraps (waste film), install the disk and lock the nut.

(2) When the winding action is skid, the five-star handle can be tightened, or remove the external fixed disk, fasten the middle of the fastening screw to increase the friction between the winding disk and the driven part, to eliminate slip.

Seven. mechanical maintenance:

Regular maintenance is the best way to maintain the mechanical life , the following is the general maintenance projects of the machine. In addition to the operators and professional maintenance person, the rest of the staff are prohibited to do the maintenance of the machinery. Make sure the power cut off before maintenance to avoid danger.

1, the pressure adjustment combination maintenance:

Pneumatic control valve maintenance: When the water tank above 2/3 of the water level, the tank should be discharged of water.

Discharge Method: Close the intake valve, and then press the bottom of the filter drain switch, you can discharge the water (Figure 7.1)

2, Everyday before working, you must use the air pressure blowing the conveyor to keep it clean.

3, When there is film stick to the sealing knife, please use a cotton towel gently remove the film (when the knife still warm). Prohibit to use of metal for scrubbing, because the metal friction will damage the protective film on the knife, loss the sealing knife function.

4, Scrap winding part maintenance:

(1) Maintenance once a month.

(2) Remove the fix nut and remove the spring and the collection wheel.

(3) Apply butter to the contact surface of the shaft and the winding wheel to keep the collection wheel running smoothly.

(4) Install back the collection wheel and spring and fix back the nut.

5, chain and sprocket maintenance: about once every three months maintenance, first remove the shield, then apply butter to the chain and sprocket. Install the cover after maintenance.

6, bearing and bearing block maintenance: about once every 3 months, the machine parts which are equipped with bearing and bearing block should apply hydraulic oil to the contact gap between the spindle and bearing, to keep the lubrication.

7, check if the cutter fixed screw is locked, if loose, please lock tight. (Once a month)

8, after a period of running, the machine belt will be loose slightly. When the belt can not be driven tightly, please adjust the belt tightness.

9, if the Teflon on the knife come off , which will make the film easily attach to the knife, the knife must be re-Teflon treatment or change the new seal knife. Check the teflon tape cover on the sealing silicone strip, if it’s damaged, need to be replaced.

10, replace the electric tube: When the electric tube burned or damaged and can not be heated, you need to replace the electric tube.

Note: that the replacement of the electric heating tube must first determine the new heating tube voltage and wattage is appropriate.

Replacement steps:

A.Turn off the power and wait for the heating tube to cool.

B. Remove the electric tube wires located in the wiring box.

C.Loose the fixing screws, remove the electric tube, and then install the new heating tube.

D.lock the fixing screw, connect the heating tube line and lock the wiring box.

11, the replacement of heat-resistant rubber:

A. turn off the power, until the electric tube cooling, tear off the heat-resistant tape (Figure 7.2).

B. Remove the heat-resistant rubber, replace the new one and make it match with the knife seat concave side, to ensure its surface is flat, and then remove the excess part.

C. Affixed the heat-resistant tape, pay attention to the tape must be flat and should not have any wrinkle.

12.Lifting screw maintenance: lifting screw maintenance once a month, first remove the rear baffle, and then apply butter to the chain, sprocket and the 4 T-type screw contact clearance, and then open the elevator up and down to adjust, so that all parts fully lubricated. After the maintenance, set the baffle back..

13, sealing knife dis-assembly and maintenance

A. Loose the fastening screws on the shield, and remove the shield.

B. Remove the thermo-couple from the heating unit, loose the screws on the connection block ,remove the knife from the upper knife holder.

C.And then tear down the set screw of heating tube inside the sealing knife, remove the heat tube.

D. clean the sealing knife; if the sealing knife wear and can not work anymore, then replace the new sealing knife.

E. to complete the above steps and then install all parts back.

Fig.7.3

Eight.troubleshooting:

1、troubles shooting instruction

| Items | Situation | Cause | Solution |
| --- | --- | --- | --- |
| 1 | Machine has no electric | Power not connected | Connect machine to |
|  |  | Power Switch close | Start the power switch |
|  |  | Power switch burned-out | Replace new switch |
|  |  | Fuse burned-out | Replace new fuse |
| 2 | Machine has electric, but machine doesn’t work | Emergency switch down | Release the emergency switch |
|  |  | （PLC）doesn’t work | check（PLC）input power |
|  |  | PLC burned-out | Replace new PLC |
|  |  | Emergency switch contact burned-out | Replace new emergency switch |
| 3 | Heater doesn’t heat | Heater Switch turn off | Turn on the heater switch |
|  |  | Default temperature is too low | Adjust the default temperature higher |
|  |  | Heater switch contact burned-out | Replace the heater switch |
|  |  | （TC）Temperature controller burned-out | Replace TC |
|  |  | （SSR）solid state relay burned-out | Replace（SSR） |
|  |  | Heating tube broken | Replace heating tube |
| 4 | Temperature can’t be controller | （SSR）broken | Replace the(（SSR） |
|  |  | Thermocuple loose or broken | Tighten the thermocuple or replace it. |
|  |  | （TC）burned-out | Replace TC |
|  |  | Heat protective relay(R7) broken | Replace R7 |
| 5 | Feeding-film motor doesn’t run | Feeding limit switch PR6 broken | Replace feeding limit switch PR6 |
|  |  | Feeding replay R5 broken | Replace relay |
|  |  | Feeding motor over-load or over-heat | Restart the feeding motor |
|  |  | Feeding motor broken | Replace motor |
| 6 | Front convey motor doesn’t work | PLC [Y1] contact damaged | Replace contact [Y1], or change PLC program or change PLC |
|  |  | Brake Controller BR1 broken | Replace brake controller BR1 |
|  |  | Front convey motor over-load or over-heat | Restart the front convey motor |
|  |  | Front conveyor motor over-load or over-heat broken | Replace the front convey motor |
| 7 | Rear conveyor motor doesn’t work | PLC[Y2] contact damaged | Replace contact[Y2] or change PLC program or change PLC |
|  |  | Brake Controller BR2 broken | Replace brake controller BR2 |
|  |  | Rear convey motor over-load or over-heat | Restart the rear convey motor |
|  |  | Rear motor over-load or over-heat | Replace rear convey motor |
| 8 | Pulling film motor doesn’t work | PLC[Y3]contact damaged | Replace contact[Y3] or change PLC program or change PLC |
|  |  | Scraps motor relayR9 broken | Replace the scraps motor relayR9 |
|  |  | Manual feeding film switch broken | Replace the Manual feeding film switch |
|  |  | Scraps motor over-load or over-heat | Restart the scrap motor |
|  |  | Scraps motor broken | Replace the scraps motor |
| 9 | Sealing device doesn’t work | Mechanical failure, gear rack get struck by foreign matter | Clear the foreign matter |
|  |  | PLC[Y4]contact damaged | Replace contact[Y4] or change PLC program or change PLC |
|  |  | Sealing solenoid valve SV1 broken | Replace solenoid valve SV1 |
|  |  | Manual sealing button broken | Replace manual sealing button broken |
|  |  | Sealing relay R13 broken,the sealing device can’t open | Replace R13 |
|  |  | Sealing relayR12 broken,the sealing device can’t open | Replace R12 |
| 10 | Sealing buzzer alarming | Knife shield press on the pack product | Take out the pack product and press manual sealing button. |
|  |  | Sealing stop suddenly and the buzzer alarming | Lower the trigger sleeve on the cutter seat slightly to the proper position, or adjust (move forwarder)the sensor on the cylinder to the appropriate position. |
| 11 | After sealing, the Film didn’t cut off,or sealing is not fastness or sealing line cracking. | Sealing time too short | Adjust sealing time, add 0.1second every time. |
|  |  | Upper&down sealing seat didn’t seal tightly | Adjust the sealing seat |
|  |  | Teflon tape damaged | Replace Teflon tape |
|  |  | Down seat rubber damaged | Replace rubber |
| 12 | Scraps pull film keep working | Electric eyes didn’t line-up | Loose the eye’s screws and make it line-up.until the eye light up and then tight the screws. |
|  |  | Electric eye broken | Replace the electric eye. |
| 13 | Side knife press on pack product | The product was not driven by the conveyor guide edge. | Place the product to the guide edge correctly. |
| 14 | Front knife press on the pack product | Delay sealing time not enough,the machine start sealing when the product still not completely through the seal seat. | Increase the time of seal timer |
|  |  | Pack product is transparent or has gap,Change the electric-eye mode. | Refer to view compensation operation |
| 15 | Front conveyor deviation run | The front driving roller unstable | Adjust the driving roller till the conveyor running normally. |
| 16 | Pull film not smooth | Wrong placement of film | Adjust the position, refer to P16 |
| 17 | Pull film doesn’t run | Scraps run into the pull roller | Clean scraps |
| 18 | Film upper or down layer offset | Balancing pole wrongly adjusted | Adjust balancing pole |
|  |  | Wrong position of film-clamp roller | Check item 16 |
|  |  | Wrong stability of the film | Replace film |
| 19 | After sealing once, the machine does not work. | Proximity switch PR5 broken or no induction | Check PR5, if it’s broken, replace it. |
| 20 | Occasionally there is phenomenon of sealing knife doesn’t reach the defaulted position. | The output point of PLC sealing time replay Y6 keep close | Replace PLC |

Nine.Circuit Diagram

Ten.Electrical Components List

1.Electrical components list 1

| Item | Name | Function |
| --- | --- | --- |
| BR1 | Brake Controller 1 | Control front conveyor motor brake |
| BR2 | Brake Controller 2 | Control rear conveyor motor brake |
| BZ | Buzzer | alarming |
| C1 | Capacitance 1 | Control front conveyor motor |
| C2 | Capacitance 2 | Control rear conveyor motor |
| C-10u | capacitance（come with motor） | Control scrape motor |
| C-10u | capacitance（come with motor） | Control lifting motor |
| C5 | Capacitance5 | Control feeding-film motor |
| F1 | Inverter | Control Pull-film motor, adjust speed |
| FU1 | Fuse | Main circuit overload or short circuit when the fuse, the protection of other electrical appliances. |
| FU2 | Fuse | Main circuit overload or short circuit when the fuse, the protection of other electrical appliances. |
| H1 | Heating Tube | Heating the front sealing knife |
| H2 | Heating Tube | Heating the side sealing knife |
| KM | Scrapes Contactor | Control scrapes motor |
| M1 | Front conveyor motor | pull the front conveyor |
| M2 | Rear conveyor motor | Pull the rear conveyor |
| M3 | Pull film motor | Pull film |
| M4 | Scrape motor | Winding scrapes |
| M5 | Feeding-film motor | Feeding film |
| M6 | Lifting motor | Control sealing knife lifting |
| PH1 | Feeding-film photoelectric switch | Feeding film detecting |
| PH2 | Detect product photoelectric switch((vertical) | Detect product |
| PH3 | Detect product photoelectric switch((horizontal) | Detect product |
| PR1 | Proximity switch | Abnormal sealing |
| PR2 | Proximity switch | Abnormal sealing |
| PR3 | Proximity switch | Abnormal sealing |
| PR4 | Proximity switch | Abnormal sealing |
| PR5 | Proximity switch | Sealing knife lift locating |
| PR6 | Proximity switch | Feeding-film induction |
| PR7 | Proximity switch | Scrape upper induction, Control scrape motor to stop when film pulling stop. |
| PR8 | Proximity switch | Scrape down induction, Control scrape motor to stop when film broken. |
| PS1 | Magnetic Switch | Sealing knife down locating. |
| QF | Low-voltage switch | Automatically switching circuit failure, to protect the main circuit from short circuit, overload and under-voltage. |
| QS | Power switch | Control power start |
| R1 | Intermediate relay | When the vertical electric eye PH2 is selected,to control the front conveyor and sealing actions stop simultaneously. |
| R2 | Intermediate relay | Emergency relay |
| R3 | Intermediate relay | Control scrapes down |
| R4 | Intermediate relay | Control scrapes up |
| R5 | Feeding-film relay | Control feeding film motor |
| R6 | Lifting relay | Control lifting motor(up) |
| R7 | Heat-protect relay | Heating protection |
| R8 | Lifting relay | Control lifting motor(down) |
| R9 | Pull-film motor relay | Control the pull-film motor |
| R12 | Intermediate relay | Control sealing Solenoid valve(down) |
| R13 | Intermediate relay | Control sealing Solenoid valve(up) |
| SA1 | Selector Switch | Heating Switch |
| SA2 | Selector Switch | Manual/Auto. Mode switching |
| SA3 | Selector Switch | Vertical/horizontal photoelectric select |
| SA4 | Selector Switch | Standard/View consumption mode switching |
| SA5 | Selector Switch | Telescopic switch reserved hole |
| SA6 | Key Switch | Open the key switch before open the safety door to operate the machine. |
| SB1 | Start-up Switch | Manual sealing |
| SB2 | Start-up Switch | Manual pull film |
| SB3 | Emergency Switch | Emergency stop |
| SB4 | Emergency Switch | Emergency stop |
| SB上 | Start-up Switch | Start lifting motor, control knife holder up. |
| SB下 | Start-up Switch | Start lifting motor, control knife holder down. |
| SQ1 | Safety Switch | Control when the safety door open, machine stop. Only operate with key. |
| SQ2 | Limit Switch | Scrape-fill alarm |
| SQ上 | Limit Switch | Control knife holder lifting limit |
| SQ下 | Limit Switch | Control knife holder decline limit |
| SSR1 | Solid state relay | Control front sealing knife heating tube temperature |
| SSR2 | Solid state relay | Control side sealing knife heating tube temperature |
| SV1 | Sealing Solenoid valve | Control lifting motor so to control sealing movement. |
| T1 | Time relay | Set pre-feeding film time |
| T2 | Time relay | Set sealing time |
| T3 | Time relay | Set delay sealing time |
| TC1 | Temperature controller | Control front sealing knife temperature |
| TC2 | Temperature controller | Control side sealing knife |
|  | Sealing cylinder | Control sealing knife action |
|  | Filter | Filtering |
|  | Power Switch | Supplying power to control circuit |
|  | Exhaust fan | Exhausting air |
| PLC | PLC | Store program, input and output instructions to control mechanical movement. |
| 1102 | Signal light | Light：main power start Light-off：main power close |

2.Electrical components list 2

| Item | Diagram | Name | Item | Diagram | Name |
| --- | --- | --- | --- | --- | --- |
| M1 |  | Front conveyor motor | PR5 |  | Sealing knife positioning proximity switch |
| M2 |  | Rear conveyor motor | PR6 |  | Feeding-film proximity witch |
| M3 |  | Pull-film motor | PR7 PR8 |  | Scraps up proximity switch--when pull film stop,control the scrape motor stop. Scrapes down proximity switch--when film broken,control scraps motor stop |
| M4 |  | Scrapes motor | SQ-up/SQ-down |  | Knife-holder up limit&down limit position |
| M5 |  | Feed-film motor | SQ2 |  | Scrapes fill alarm |
| M6 |  | Sealing knife holder lifting motor |  |  | Sealing cylinder |

# Text boxes

Five-start Handle

Handle screw with white sealing tape

Rubber roller

Needle(pin) rollers

Height Adjustment Nut

Air Pressure Adjustment

Lock nut

Intake Valve

Figure 4.1

Figure4.2

Figure 5.1

W

H

L

Handle A

tripod

Handle D

Guide Rod

Handle C

Hnadle B

Figure 5.2

Figure 5.3

½H

H

Blade height scale

figure5.4

scale

Position-fix Rod A

Lock handle

Film open side

Film feed roller

Position-fix rod B

figure5.5

H1

½ H1

Figure 5.6

5.7D fixing handle

5.7A  Handle

5.7C Pin Roller

5.7B  Rubber roller

Figure5.7

Diagram 5.2

Scrape roll

Fig.5.8

Packed product

Front  Seal Knife

Fig5.10

Feeding Direction

Fig5.9

Packed product

Photoelectric

Down Knife Seat

Sealing Line

Fig.5.11

PH3

PH1

PH2

Electric eye

Packed Product

Packed Product

Electric eye

View Consumption Mode

Standard mode

Proximity switch

Swing Arm

Tighten Handle

Rolling axle

Swing Arm

Fig A

FigB

Scale

screw

Proximity switch

Handle

Fig.6.1

Fig.6.2

Rotate shaft

screw1

screw2

Fig6.3

screw1

screw2

Fig6.4

Air pipe

Fix screws

shield

Sealing blade

PS1Magnetic Switch

Knife holder

shield

Proximity switch

Trigger roller

nut

Fasten screw

Winding roller

Fig.A

Fig.B

Figure6.7

Air inlet

filter

Bottom nut

Fig.7.1

Down Knife Holder

Figure7.2

Heat-resist Tape

Knife Holder

Heat-resist Rubber

Knife holder

Fix Screw

Thermocouple

Connection Block

Heat Tube Location Hole

Shield

Figure7.4